## Slide 1: Scaling Trapped Ions for Atomic Clocks and Quantum Computing
SAND2023-11268C
Megan Ivory
Sandia National Laboratories
Quantum Learning Lab
September 29, 2025
Sandia HOA-2 (photo credit:UMD)

## Slide 2: Quantum is already all around us
Photos from: IQC quantum applications today;
WAYKEN laser welding; NS medical devices
Lasers rely on the quantized energy levels in atoms to produce a highly focused beam of light.
Solar Cells convert light into an electric current, a process known as the photovoltaic effect.
Magnetic Resonance Imaging uses “spin” to create non-invasive 3D imagine of the body.
Electron Microscopes use electrons instead of light as an illumination source, which provide better resolution than optical microscopes.
Atomic Clocks rely on the quantized energy levels in atoms to accurately measure time for geolocation.

## Slide 3: Many Quantum Applications are within reach
Quantum Sensing
Quantum Communication
Quantum Computing
Time
Atomic Clocks
Magnetic Fields
Magnetometers
Gravitational Fields
Gravimeters
Accelerations
Inertial Navigation
Algorithms
Benchmarking
Error Correction
Annealing
Gate-based Quantum Computing
Quantum Networks
Quantum Repeaters
Quantum Key Distribution
Cryptography

## Slide 4: There are lots of Quantum Technologies to choose from!
Neutral Atoms
Superconducting Josephson Junctions
Trapped Ions
Photons
Spin Qubits
Photo: QuEra
Photo: USTC
Photo: Princeton
Photo: IBM
Photo: Sandia HOA-2 (UMD)

## Slide 5: QIS at Sandia National Laboratories
Sandia has been investing in a huge breadth of quantum and quantum enabling technologies for 15+ years​
Multiple qubit technologies: Ion traps​, Neutral atoms​, Silicon spin qubits, superconducting Josephson junction qubits
Multiple quantum sensing projects: clocks, magnetometers, electric field sensors, inertial sensors
Emerging technology: Diamond vacancies​
Enabling technology: Silicon & III/V photonics spanning UV to SWIR​
Existing collaborative quantum research projects​
QSCOUT – Trapped Ion User Testbed​
Quantum Systems Accelerator
Neutral atom quantum computation experiment​
MEG – Magnetoencephalography for brain studies​
Photonic Quantum Computing Testbed
Quantum workforce from K-12 through early career scientists
60+ photonic staff, 150+ quantum staff​
MEG with optically pumped magnetometers​
Borna et al. Plos one 15.1 (2020)​
Trapped Ion Surface Trap
NV magnetic imaging of ​electronic circuit behavior​ Kehayias et al. Phys. Rev. Applied 17:014021 (2022)​
​

## Slide 6: There are lots of Quantum Technologies to choose from!
Superconducting Josephson Junctions
Trapped Ions
Spin Qubits
Photo: QuEra
Photo: USTC
Photo: Princeton
Photo: IBM
Photo: Sandia HOA-2 (UMD)
Let’s talk about charged atoms
(aka ions)
for atomic clocks and quantum computing!
Neutral Atoms
Photons

## Slide 7
Shor’s Algorithm
Can factor large numbers more efficiently than classical algorithms.
This could break RSA encryption.
1,274,093,332,123,426,680,869 =
???,???,???,??? x ?,???,???,???
Why do we care about quantum computing?
Notes: RSA often used to pass symmetric key encryption
Most efficient classical alg: number field sieve. Runtime is exponential in N (where N uses log_2 N bits)
Shor’s algorithm is polynomial in N. RSA is alos vulnerable to elliptic curve and Diffie-hellman algorithms.
2017: NIST had a post quantum crypto contents to find PQC algorithms for public-key encryption and digital signatures. Winners announced in 2022, including a lattice-based algorithm (NP-hard)
Yilei Chen posted a paper April16 that reduced the scaling of lattice problems from exponential to polynomial
Eprint.iacr.org/2024/555.pdf  there was a bug discovered a few days later (whew!)
**few absolute proofs of the post-quantum security of algorithms
Nitrogen fixing
Fusion calculations for DOE
Financial algorithms

## Slide 8
Shor’s Algorithm
Can factor large numbers more efficiently than classical algorithms.
This could break RSA encryption.
1,274,093,332,123,426,680,869 =
135,763,451,261 x 9,384,656,329
Shor’s algorithm is an exponential speed-up over classical algorithms
Why do we care about quantum computing?
Notes: RSA often used to pass symmetric key encryption
Most efficient classical alg: number field sieve. Runtime is exponential in N (where N uses log_2 N bits)
Shor’s algorithm is polynomial in N. RSA is alos vulnerable to elliptic curve and Diffie-hellman algorithms.
2017: NIST had a post quantum crypto contents to find PQC algorithms for public-key encryption and digital signatures. Winners announced in 2022, including a lattice-based algorithm (NP-hard)
Yilei Chen posted a paper April16 that reduced the scaling of lattice problems from exponential to polynomial
Eprint.iacr.org/2024/555.pdf  there was a bug discovered a few days later (whew!)
**few absolute proofs of the post-quantum security of algorithms
Nitrogen fixing
Fusion calculations for DOE
Financial algorithms

## Slide 9
Shor’s Algorithm
Can factor large numbers more efficiently than classical algorithms.
This could break RSA encryption.
1,274,093,332,123,426,680,869 =
135,763,451,261 x 9,384,656,329
Shor’s algorithm is an exponential speed-up over classical algorithms
Grover’s Algorithm
Can search an unsorted database more efficiently than classical algorithms.
Sqrt speedup.
Name | Phone
Alice | 314-1592
Bob | 271-8281
Charlie | 105-4571
Dave | 885-4187
Eve | 125-6637
Frank | 299-7924
Chemistry & Pharma
Catalyst & enzyme design, drug discovery, bioinformatics, genomics, patent diagnosis, improved MRI
Information Technology
Cybersecurity, machine learning, AI, search, software verification & validation
Finance
Portfolio optimization, asset pricing, risk analysis, trading strategies, fraud detection, market simulation
Other Industry
Materials, OLEDs, composites, logistics, scheduling, semiconductor device design, chip layout
Energy
Mineral & oil exploration, oil well optimization, energy distribution, battery & solar cell design
Why do we care about quantum computing?
Notes: RSA often used to pass symmetric key encryption
Most efficient classical alg: number field sieve. Runtime is exponential in N (where N uses log_2 N bits)
Shor’s algorithm is polynomial in N. RSA is alos vulnerable to elliptic curve and Diffie-hellman algorithms.
2017: NIST had a post quantum crypto contents to find PQC algorithms for public-key encryption and digital signatures. Winners announced in 2022, including a lattice-based algorithm (NP-hard)
Yilei Chen posted a paper April16 that reduced the scaling of lattice problems from exponential to polynomial
Eprint.iacr.org/2024/555.pdf  there was a bug discovered a few days later (whew!)
**few absolute proofs of the post-quantum security of algorithms
Nitrogen fixing
Fusion calculations for DOE
Financial algorithms

## Slide 10: Why do we care about better atomic clocks?
Atomic clocks make modern life possible…
How accurate do the clocks need to be for your GPS to work?
If the clocks changed by .00004 s in a day,
or 0.015 s in a year,
or 1.5 s in 100 years,
your location would be off by 6 miles.
https://www.youtube.com/watch?v=hzLTgtFaPLY
Notes: End: 12:00 min

## Slide 11: Why do we care about better atomic clocks?
Two choices today:
Tiny clocks that perform ok -vs- Room sized clocks that are the best in the world
Photo credit: NIST (left) and (c) 2019 Katori et al. (right)
Chip Scale Atomic Clock –
1 lost second every 16,000 years
Optical Atomic Clock –
1 lost second every 300,000,000,000 years
Notes: End: 12:00 min

## Slide 12: Trapped Ions as Qubits and Clocks
Energy = ℏ𝜔
Energy transition is proportional to frequency (1/time).
We tune electromagnetic radiation to the exact frequency to excite an electron.
Scale down size, weight, and power (SWaP),
Maintain 10-14/√𝜏
Goals:
Clocks:
Information is encoded into an electron state.
We use electromagnetic radiation to control the electron state.
Scale up number of qubits,
Improve gate fidelity,
Add system capabilities
Goals:
Qubits:
|1⟩
|0⟩
Notes: EOS 5:45

## Slide 13: Outline
Confining Potential
  From “macroscopic” 3D to microfabricated surface traps
Light Delivery
  From free space to integrated photonics
Ultrahigh Vacuum
  From bulky COTS to compact and integrated
Notes: 9:30

## Slide 14: Trapped Ion Science is a Team Sport!
Fabrication
Matt Delaney
Ray Haltli
Ed Heller
Jeff Hunker
Tipp Jennings
Nick Jimenez
Becky Loviza
Zach Meinelt
Chris Nordquist
Eric Ou
John Rembetski
Corrie Sadler
Ben Thurston
Theory/Software
Josh Goldberg
Andrew Landahl
Ben Morrison
Tim Proctor
Kenny Rudinger
Antonio Russo
Brandon Ruzic
Jay Van Der Wall
Kevin Young
This work is supported by the Defense Advanced Research Projects Activity (DARPA). Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
Experimentalists
Todd Barrick
Ashlyn Burch
Matt Chow
Susan Clark
Craig Hogle
Megan Ivory
Joon Kwon
Dan Lobser
Hayden McGuinness
Melissa Revelle
Theala Redhouse
Will Setzer
Jon Sterk
Dan Stick
Chris Yale
Engineering
Dave Bossert
James Burkart
Mike Gehl
Nick Karl
Rex Kay
Madelyn Kosednar
Stefan Lepkowski
Chris Nordquist
Brad Salzbrenner
Bill Sweatt
Ted Winrow
Summer 2023 Interns
Jae Ho Han
Brian Matthews
Koray Mentesoglu
Aria Stevens

## Slide 15: Confining potential with microfabricated surface traps

## Slide 16: Source of atoms, typically an “oven”
ytterbium

## Slide 17: How to confine an ion

## Slide 19: Ion Trapping Essential #1: Confining Potential
Courtesy of Wes Campbell
DC
DC
RF
RF
“Four Rod Trap”
“Blade Trap”
Ions are charged, which makes them easy to confine with electric fields.
Earnshaw’s Theorum: You cannot trap with static electric fields.
Instead, use an RF voltage.

## Slide 20: Microfabricated Surface Traps
DC
DC
RF
RF
RF
RF
DC
DC
DC

## Slide 21: Microfabricated Surface Traps
RF
RF
DC
DC
DC
House, PRA 78 033402 (2008)
RF
RF
DC
DC
DC
Manufacturable and reproducible
Control over ion positioning, stray fields, etc
Multi-layer capabilities for routing and unique geometries
Overhung electrodes for reduced line-of-site to dielectric
Low SWaP
Reliable and consistent operation
Long ion lifetimes
High fidelity gate operations
(photo credit:UMD)

## Slide 22: Microfabricated surface traps for clocks and computing
Chip-based (low size and weight).
Because the ions are confined close to the surface, less RF power is required (low power).
Low SwaP  More deployable
Also enables multi-ensemble clock protocols
Clocks:
Sandia’s traps are used in quantum computers around the world, including IonQ and Quantinuum.
QSCOUT has 5 fully connected qubits:
Single-qubit gates: <10 us, 99.5% fidelity
Two-qubit gates: ~200 us, 98% fidelity
Qubits:

## Slide 23: Light Delivery with Integrated Photonics

## Slide 24: Doppler/laser cooling
Excited State
Ground State
> 600 mph to < 1 mph… in < 0.01 s

## Slide 25: Ion Trapping Essential #2: Light Delivery (for 171Yb+)
2S1/2
2P1/2
369 nm
3[3/2]1/2
2D3/2
935 nm

## Slide 26: Ion Trapping Essential #2: Light Delivery (for 171Yb+)
2S1/2
2P1/2
369 nm
3[3/2]1/2
2D3/2
935 nm
Quantum Computing
F=0
F=1
355
nm
Extremely long lived excited state

## Slide 27: Ion Trapping Essential #2: Light Delivery (for 171Yb+)
F=0
F=1
2S1/2
2P1/2
369 nm
3[3/2]1/2
2D3/2
935 nm
Atomic Clock
F=1
F=2
435 nm
Narrow transition @ Optical frequency
ν0 = 688 THz
Δν = 3 Hz
Q = 2 x 1014

## Slide 28: Ion Trapping Essential #2: Light Delivery (for 171Yb+)
F=0
F=1
2S1/2
2P1/2
369 nm
3[3/2]1/2
2D3/2
935 nm
Quantum Computing
355
nm
Extremely long lived excited state
Atomic Clock
F=1
F=2
435 nm
Narrow transition @ Optical frequency
ν0 = 688 THz
Δν = 3 Hz
Q = 2 x 1014

## Slide 29: Necessary elements of a trapped ion quantum computer
University of Oxford Trapped Ion Lab

## Slide 30: Integrated waveguides for visible – IR light delivery
Emerging Quantum Technologies
  Multi-layer traps: top metal layer for RF and DC electrodes, overhangs underlying SiO2 to avoid direct line-of-sight to dielectrics
  Silicon nitride waveguides for visible/IR light delivery
  Alumina waveguides for UV light delivery
  In and out coupling via diffraction gratings or edge coupling
  Added Al reflector to improve output efficiency
M. Ivory, et al, Phys. Rev. X 11, 041033 (2021)
Chip

## Slide 31: Integrated phtonics for visible – IR light delivery
Emerging Quantum Technologies
  Multi-layer traps: top metal layer for RF and DC electrodes, overhangs underlying SiO2 to avoid direct line-of-sight to dielectrics
  Silicon nitride waveguides for visible/IR light delivery
  Alumina waveguides for UV light delivery
  In and out coupling via diffraction gratings or edge coupling
  Added Al reflector to improve output efficiency
  We can also add integrated detectors for readout
Chip
WG
WG
FS
RF
DC
935
760
435
369
Loading Hole
SPAD
369nm
760nm

## Slide 32: Integrated photonics for clocks and computing
Eliminates bulky free space optics which reduces size and weight.
Enables multi-ensemble clock protocols.
Eliminates need for optical access through vacuum chamber.
Increases stability in presence of vibrations  deployability.
Clocks:
Compatible with high fidelity gates.
Can enable larger qubit size within same volume via 2D trap arrays.
Silicon nitride and alumina waveguides allow reasonable efficiency for UV to IR wavelengths.
QSCOUT has explored waveguide compatibility with 355 nm pulses.
May increase stability for higher fidelity operations
Qubits:

## Slide 33: Compact Ultrahigh Vacuum Systems

## Slide 34: Ion Trapping Essential #3: Ultrahigh Vacuum
UHV pressures ~10-11 Torr allow us to trap our ion for long periods of time without atmospheric collisions
Electrical feedthroughs for DC and RF
Imaging with camera or PMT for readout
Vacuum pumps
Laser Access
Laser Access
Notes: EOS 14:00

## Slide 35: Compact ultrahigh vacuum systems
R. Spivey, et al, IEEE Trans. on Quant. Phys.. 3, 5100111 (2021)
(photo credit:UMD)
Enabled by microfabricated surface traps
Driven by the need for longer ion lifetimes, typically limited by vacuum quality
Compact UHV packages can fit inside cryostats where 4-10K temps freeze out many atmospheric collisions

## Slide 36: Compact ultrahigh vacuum systems
R. Spivey, et al, IEEE Trans. on Quant. Phys.. 3, 5100111 (2021)
(photo credit:UMD)
ColdQuanta
Enabled by microfabricated surface traps
Driven by the need for longer ion lifetimes, typically limited by vacuum quality
Compact UHV packages can fit inside cryostats where 4-10K temps freeze out many atmospheric collisions

## Slide 37: Compact ultrahigh vacuum systems for clocks and computing
(photo credit:UMD)
Enables longer lifetimes for larger qubit numbers via cryo pumping.
Qubits:
Decreases SWaP  deployability.
Further reduction in size if integrated photonics eliminate the need for viewports and/or optical feedthroughs.
Further reduction in size if electronic signals can be routed external to the vacuum system (no electrical feedthroughs).
Clocks:

## Slide 38: Compact vacuum systems
2.3E-11 Torr in custom compact vacuum package
Sufficient for long ion lifetimes in the final clock demonstrator
Edge coupling can happen in atmosphere
Notes: EOS 43:00

## Slide 39: Recap
“Macroscopic” 3D to microfabricated surface traps for confinement
  Enables manufacturability, reproducibility, control, and low SWaP
Light Delivery with integrated photonics
  Enables multi-ion addressing in 2D geometries
  Increases beam stability and deployability
Compact, Integrated Ultrahigh Vacuum systems
  Enables longer ion lifetimes due to compatibility with cryo systems
  Significant reduction in SWaP is feasible
Notes: 7:00

## Slide 40: Thank you!
Fabrication
Matt Delaney
Ray Haltli
Ed Heller
Jeff Hunker
Tipp Jennings
Nick Jimenez
Becky Loviza
Zach Meinelt
Chris Nordquist
Eric Ou
John Rembetski
Corrie Sadler
Ben Thurston
Theory/Software
Josh Goldberg
Andrew Landahl
Ben Morrison
Tim Proctor
Kenny Rudinger
Antonio Russo
Brandon Ruzic
Jay Van Der Wall
Kevin Young
This work is supported by the Defense Advanced Research Projects Activity (DARPA). Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
Experimentalists
Todd Barrick
Ashlyn Burch
Matt Chow
Susan Clark
Craig Hogle
Megan Ivory
Joon Kwon
Dan Lobser
Hayden McGuinness
Melissa Revelle
Theala Redhouse
Will Setzer
Jon Sterk
Dan Stick
Chris Yale
Engineering
Dave Bossert
James Burkart
Mike Gehl
Nick Karl
Rex Kay
Madelyn Kosednar
Stefan Lepkowski
Chris Nordquist
Brad Salzbrenner
Bill Sweatt
Ted Winrow
Visit the QSCOUT website: https://qscout.sandia.gov
or email qscout@sandia.gov
Ask about summer internships:
www.sandia.jobs/jobs
mkivory@sandia.gov
Or come talk to me!